## Slide 1: Year 10 Microprocessor Control
INPUT DEVICES (Sensors)
Sensors feed information into the process blocks of the control system by reacting to environmental changes around them.
Digital sensors are essentially simple on / off switches.
Analogue sensors are usually specialised forms of electronic resistors.
Digital
Analogue
When these sensors are activated they switch on or off. There is no gradual change in their state. It is one or the other.
Sensors are divided into groups or categories.
These sensors are able to react to gradual changes in their local environment. They react to environmental changes by gradually changing their electrical resistance.
These are most commonly used as positional sensors because they usually react to something being there or not being there.
These are most commonly use to detect gradual environmental changes such as light levels, temperature changes, volume levels and tension.
Examples of Digital Sensors:
Microswitches - Pressure
Reed Switches - Magnetism
Photo Transistors - Light
Pressure Pad - Pressure
Examples of Analogue Sensors.
Thermistors - Temperature
LDR - Light
Microphone - Sound
Strain Gauge - Tension

## Slide 2: Year 10 Microprocessor Control
Digital and Analogue OUTPUT DEVICES (Electrical components that can be switched on or off by the process blocks )
OUTPUT devices are electrical components that are switched on/off by the process blocks which are responding in a predetermined (pre-programmed) manner to one or more INPUT signals.
Digital OUTPUT devices are either on or off. There is no inbetween state.
Analogue OUTPUT devices can be controlled by the gradual increase or decrease in electrical power to them.
Digital
Analogue
These are most commonly used as warning devices or power sources that do not need to vary in speed
These are most commonly use to detect gradual environmental changes such as light levels, temperature changes, volume levels and tension.
Examples of Digital OUTPUT Devices.
LED - Light
Buzzers - Sound
Solenoids - Magnetism
Stepper Motors - Movement
Examples of Analogue OUTPUT Devices.
Heaters - Temperature
Speaker - Sound
Electric Motor - Movement
Filament Bulb - Light