## Slide 1
introducing to lOGIc gates
This easiest way to understand logic gates is to think of them as a series of on/off switches in an electronic circuit.
There are many types of logic gates but at IGCSE level we only need to know about the 3 most common ones.
Example One.
Here is a simple electronic circuit, it has a battery as the power supply, 2 push-to-make switches (A & B) and a light bulb
Question
What must you do to make the bulb light up?
Answer
Press A & B at the same time
This is an example of an AND GATE. In order for the bulb to light up both A AND B have to be switched on.
In electronic terms switch A would be an INPUT signal from a sensor and switch B would be a another INPUT signal from a second sensor.
If INPUTS A AND B were both switched on then the light bulb OUTPUT would be on.

## Slide 2
introducing to lOGIc gates
The simple circuit from the previous slide is an example of an AND Gate.
The correct symbol for an AND Gate is…..
INPUT signal A
INPUT signal B
OUTPUT signal
Technical Terms
In electronics there are a number of ways to describe when an input or output signal is on or off. It is important to know them all.
ON can be described as a state HIGH
ON can be described as the number 1
ON can be described as True
OFF can be described as a state LOW
OFF can be described as the number 0
OFF can be described as False
When working out how a Logic Gate functions in a circuit you use a system called a TRUTH TABLE.

## Slide 3
introducing to lOGIc gates
INPUT signal A
INPUT signal B
OUTPUT signal
Technical Terms
ON can be described as a state HIGH
ON can be described as the number 1
ON can be described as True
OFF can be described as a state HIGH
OFF can be described as the number 1
OFF can be described as False
Truth table for an AND gate |  | 
INPUTS |  | OUTPUT
A | B | 
Refer to the all of the information above in order to complete the blank Truth Table for the AND gate.
0
1
0
0
0
0
0
0
1
1
1
1

## Slide 4
introducing to lOGIc gates
Technical Terms
Truth table for an OR gate |  | 
INPUTS |  | OUTPUT
A | B | 
0
0
0
1
1
1
1
1
1
Example Two.
This simple electronic circuit has a battery as the power supply, 2 push-to-make switches (A & B) and a light bulb.
Question
What must you do to make the bulb light up?
Answer
Press switch A OR switch B
This simple circuit is an example of an OR Gate.
INPUT signal A
INPUT signal B
OUTPUT signal
0
Refer to the all of the information above in order to complete the blank Truth Table for the OR gate.
1
0

## Slide 5
introducing to lOGIc gates
Technical Terms
1
With this type of logic gate the OUTPUT does the OPPOSITE to the INPUT.
Answer
Press switch A
0
1
0
Example Three.
This simple electronic circuit has a battery as the power supply, 1 push-to-break switch and a light bulb. In this circuit the OUTPUT is normally on.
Question
What must you do to make the bulb go off?
This simple circuit is an example of a NOT Gate.
INPUT
A
OUTPUT
B
Now complete the blank Truth Table for the NOT gate.
NOT Gate | 
INPUT | OUTPUT

## Slide 6
Did you know?
George Boole Inventor of the idea of logic gates. He was born in Lincoln, England and he was the son of a shoemaker in a low class family.
George Boole,
(1815-1864)
Learning Objectives:
To understand the functions of logic gates.
2. To apply gained knowledge and design your own girlfriend or boyfriend chooser using the logic gates.
LOGIc gates
Notes: About G. Boole:
http://www.google.co.uk/imgres?imgurl=http://library.thinkquest.org/C0126120/boole.jpg&imgrefurl=http://
http://www.kerryr.net/pioneers/boole.htm

## Slide 7
A logic gate is a digital circuit which either allows a signal to pass through it or to stop it.
There are seven basic logic gates: AND, OR, XOR, NOT, NAND, NOR, and XNOR.
BUT WE ARE ONLY CONCERNED WITH THESE
THREE
Did you know?
Logic gates allow the computer to do things such as add, divide, multiply, do simple yes and no reasoning in certain situations along with other things.
?Logic !
OR
AND
NOT
Notes: http://www.kpsec.freeuk.com/gates.htm
Note that logic gates are not always required because simple logic functions can be performed with switches or diodes:Switches in series (AND function)Switches in parallel (OR function)Combining IC outputs with diodes (OR function)

## Slide 8
OR
GATE
FRONT DOORBELL
SWITCH
BACK DOORBELL
SWITCH
DOORBELL
OR
GATE
Input
Input
Output
ON/OFF
ON /OFF
ON/OFF
An OR gate can have two or more inputs.
The output will be positive (True) if at least one input is true.
Y = A OR B
Notes: The output is "true" if either or both of the inputs are "true." If both inputs are "false," then the output is "false.”
It is doesn’t matter if one input will be off- the output will be on
http://www.kpsec.freeuk.com/gates.htm

## Slide 9
c
AND
GATE
AND
GATE
ON SWITCH
FOR ALARM
PERSON SENSOR
BURGLAR ALARM
Input
Input
Output
ON/OFF
ON /OFF
ON/OFF
An AND gate can have two or more inputs.
The output will be positive (true) when both inputs (the input one AND the input two) are positive (true).
Y = A AND B
Notes: The output is "true" when both inputs are "true.” Otherwise, the output is "false."
If one input will be off – the output will be off as well.
http://whatis.techtarget.com/definition/0,,sid9_gci213512,00.html

## Slide 10
To add more sensors to alarm
OR
GATE
AND
GATE
BEDROOM
SENSOR
FRONT ROOM
SENSOR
BURGLAR
ALARM
ON SWITCH
FOR ALARM
ON or OFF ?

## Slide 11
NOT
GATE
Input
Output
NOT
GATE
HEAT DETECTOR
(ABOVE 20 C)
CENTRAL
HEATING
ON
ON
OFF
OFF
A NOT gate (inverter) has only one input.
It reverses the logic state.
Y = NOT A
Notes: NOT gate has only one input. It reverses the logic state.
If the input will be on – the output will be off
If the input will be off –the output will be on.

## Slide 12
OR
GATE
AND
GATE
AND
GATE
NOT
GATE
ON
ON
OFF
OFF
FINAL
OUTPUT
ON ? OFF ?
Is the Final Output ON (True)
or OFF (false) ?

## Slide 13
girlfriend/boyfriend Chooser:
?
?
?
?
ON
YES,
She/He is OK
Good dancer
Good at sport
Blue eyes
Has a big nose
Name the logic gates. Test it by answering True or false (Yes or No) for each Input.

## Slide 14
ON
YES,
She/He is OK
Design your own girlfriend/boyfriend Chooser
By writing your own things in the Input boxes. You can choose the logic gates you have learnt. Name the logic gates. Test the Chooser by answering Yes or Not ( True or false ).

## Slide 15
1.
2.
3.
6.
4.
5.
?
ON
ON
?
ON
OFF
?
ON
OFF
?
ON
OFF
OFF
?
ON
OFF
OFF
?
ON
ON
OFF
The output is ON or OFF ?
Test 1:
Notes: 1- off, 2- on, 3-off, 4- on, 5-off, 6-on

## Slide 16
Test 2:
?
8.
9.
10.
ON
ON
ON
?
ON
ON
ON
ON
ON
ON
?
ON
ON
ON
ON
OFF
OFF
OFF
OFF
OFF
?
7.
ON
OFF
OFF
The output is ON or OFF ?
Notes: 7- on, 8-off, 9-off, 10- on